## Slide 1: Garage Door Monitor
Yes, the door is really Closed

## Slide 2: Why do I need a Garage Door Monitor?
We forget to close the door… again
I like gadgets and data
I wanted to have a record of when the door opened and closed

## Slide 3: Garage Door Monitor Logic
State Diagram
  Helpful to understand what you need to code
  States used in code:
    Opened - 1
    Closed - 3
    Auto-Closed - 4
    Reboot – 9
    Error – 8
      Only for an invalid doorstatus
    Operating - 2

## Slide 4: Version 1.0

## Slide 5: Components
NODEMCU
ESP826612E
Door Open Sensor
Door Closed Sensor
Google Sheet
Open, Closed, Operating
Calculate time since last state change
Google Script
Door Operate Relay
Other I/O

## Slide 6: Code and Connections
GarageDoorMonitor.ino
GarageDoorMonitor.gs
GarageDoorRecord (sheet)
HTTPS address of Google Sheet (SPID)
GDM (Endpoint)
HTTPS address of Google Script
GDM (Device)
Device ID

## Slide 7: Tasks
Create the Google Sheet
  Header names and Sheet name are important
  Publish and note the URL
Create the Google Script
  Add the Sheet ID into the script
  Run Setup once to add the SPID as a Key
  Use ARC (Advanced Rest Client) Chrome extension for testing (Note not all JSON seems to get passed to the Script)
Using Thinger.io
  Define the Device
    NODEMCU software will need the ID
  Create the HTTP Endpoint
    Thinger.io will need to know Device and Google Script URL
Create the Code for the NODEMCU in the Arduino IDE

## Slide 8: Thinger.io Device and HTTP Endpoint
Device: GDM
  Connects NodeMCU to Thinger.IO
Endpoint: GDM_JSON
  Endpoint is the connection between the Thinger.IO and Google Script

## Slide 9: Google Sheets
Can be programmed from Google Script
Viewable from any device
Allows data capture and analysis
Free
Create a sheet
Column headers will be used to capture data from IoT device
- State & GDMTime
Note the ID from the URL

## Slide 10: Google Script Logic
Google script is responding to an HTTPS request that is to run this script and process the enclosed JSON payload
Open and lock the Google Sheet
Functions for POST or GET response
handleResponse
  Compares the headers in the Sheet to the JSON value keys and populates the spreadsheet with the values
  Other header values are entered as functions or calculated values
  Sheet is unlocked and closed
  Test with ARC to see response.

## Slide 11: Google Script
Javascript – lots of help available
Use ARC (Advanced Rest Client) plugin for Chrome to test Javascript decode of JSON payload (simulate data from IoT broker)
Example: {"state":2,"GDMtime":"858881"} is the ‘payload’ sent through the system from the ESP8266 through Thinger.io to the Google Script.
Google Script is very sensitive to processing the JSON data
  Hard to debug
  See script for a process that worked with Thinger.IO HTTP Endpoint

## Slide 12: Version 2.0

## Slide 13: Why Version 2?
ESP8266 https does not redirect or seem to work with google script
Thinger.io HTTP endpoint can work great, but is hard to repeat a setup
  My initial setup works very reliably, but was tough setup and I could not duplicate
  Ran for 3 months with no failure or reboot.
Google script calls from HTTPS are hard to validate and debug.
Since I could not repeat the setup I was using, I decided to pursue a variation
  Maker Endpoint with IFTTT
New Requirements
  Create a stable and repeatable system.
  Capture the Status and time parameter with IFTTT to sheet
  Send a message if door auto-closes or reboots.
  Set the stage for updating the module for remote open/close and permitted open time value.

## Slide 14: Components V2
NODEMCU
ESP826612E
Door Open Sensor
Door Closed Sensor
Google Sheet
Door Operate Relay

## Slide 15: Code and Connections V2
GarageDoorMonitor2.ino
GarageDoorRecord (sheet)
GDM2 (Endpoint)
GDM2 (Device)
Device ID

## Slide 16: Tasks V2
Using Thinger.io - https://thinger.io/
  Define the Device
    NODEMCU software will need the ID
  Create the IFTTT Maker Channel Trigger Endpoint
    This can then do several things
      Add information to the Spreadsheet
      Send a message if it reboots or auto-closed the door.
Create the Code for the NODEMCU in the Arduino IDE
Create a GIT repository for the project
  https://github.com/Peterh226/GarageDoorMonitor
Publish Project on Instructables

## Slide 17: IoT Device
NODEMCU (~$8 Amazon, ~$6.50 Banggood)
  Built-in USB simplifies everything
  Reset, Program switches
  Built-in LED (used for a heartbeat monitor)
  Inexpensive and easy to use
Programming
  Used Arduino IDE
  https://github.com/esp8266/Arduino
Used various other utilities to flash and play around with NODEMCU
  NODEMCU Flasher - http://www.nodemcu.com
  LuaLoader - http://benlo.com/esp8266/index.html#LuaLoader
  ESPlorer - http://esp8266.ru/esplorer/

## Slide 18: Circuit

## Slide 19: 3D CAD Models
Solidworks
  Controller Housing
  Switch mounting brackets
  Bench-test platform
3D Printed w/SLA